SECTION 32 94 00

I-SYS® STAINLESS STEEL CABLE PLANT SUPPORT SYSTEM

Show hidden Specifier Notes for best results

FacadeScape™ Brand stainless steel plant support system by:

Carl Stahl-DecorCable Innovations LLC;

660 W. Randolph St.

Chicago, IL USA 60661

Phone:  800-444-6271

Fax: 312-474-1789

E-mail: sales@decorcable.com

Web: www.decorcable.com

This Product Specification is written in accordance with the Construction Specifications Institute (CSI) Format , including MasterFormat, SectionFormat and PageFormat. Optional text is indicated by brackets [ ]; delete optional text in final copy of specification. Specifier Notes are shown in red typically precede specification text; delete Specifier Notes in final copy of specification.

This Section specifies stainless steel cable plant support (trellis) system marketed under the FacadeScape™  tradename. Revise section number and title below to suit project requirements, local building codes, specification practices and section content. Refer to CSI MasterFormat for other section numbers and titles.

© 2006 Carl Stahl-DécorCable Innovations LLC

PART 1 GENERAL

# SUMMARY

## Section Includes:

### Stainless Steel Wire Rope Assemblies

### Stainless Steel Fittings, Anchors, Hardware, and Accessories

## Related Sections:

Specifier Note: Edit following list according to project requirements.

### Section 4 - Masonry Anchoring and Reinforcing

### Section 5 – Stainless Steel Wire Rope Assemblies

### Section 32 – Site Improvements

### Section 32 – Planting Accessories

# SYSTEM DESCRIPTION

## Performance Requirements: Provide Stainless Steel Cable Railing System and mounting hardware which have been manufactured and installed to meet or exceed manufacturer’s and project performance criteria.

# SUBMITTALS

Specifier Note: This Section includes submittal of relevant data to be furnished by Contractor before, during or after construction. Coordinate this article with Architect’s and Contractor’s duties and responsibilities in Conditions of the Contract and Division 1 Submittal Procedures Section.

## Submit listed submittals in accordance with Conditions of the Contract and Division 1 Submittal Procedures Section.

## Product Data: Submit Manufacturer’s product data sheet for specified products.

## Shop Drawings: Show layout, sizes, dimensions, details, and installation of railing frame components. Include Details of rope attachment, tensioning methods, hardware, and tensioning and mounting methodology.

## Samples: Submit samples of rope and/or hardware, as required by specifier.

## Quality Assurance/Control Submittals:

### Test reports: Submit any test report demonstrating compliance with intended use and code requirements.

### Certificates: Submit manufacturer’s certificate that product meets or exceeds specified requirements

## Closeout Submittals: Submit the Following:

### Warranty: Submit manufacturer’s standard warranty documents

### Maintenance Data: Include manufacturer’s standard cleaning and maintenance instructions to avoid detrimental actions to finishes and performance.

# QUALITY ASSURANCE

Specifier Note: This Section should include prerequisites, standards, limitations and criteria that establish an overall level of quality for products and workmanship for this section. Coordinate with Division 1 Quality Assurance Section.

## Qualifications:

### Installer Qualifications: Installer should be experienced in performing work of this section and should have specialized in installation of work similar to that required for this project.

### Specifier Note: Paragraph below should list obligations for compliance with specific code requirements particular to this section. General statements to comply with a particular code are typically addressed in Conditions of the Contract and Division 1 Regulatory Requirements Section. Repetitive statements should be avoided.

## Regulatory Requirements and Approvals:

### [Code Agency Name]

#### [Report or Approval Description]

## Mock-Ups: Install at project site or appropriate location a job mock-up using acceptable products and manufacturer approved installation methods. Obtain Owner’s and Architect’s approval of product, application, and workmanship standards. Comply with Division 1 Quality Control (Mock-Up Requirements) Section.

Specifier Note: Edit paragraph below when specifying mock-up requirements.

### Mock-Up Size: [Specify mock-up size and fixation requirements].

### Maintenance and Disposal: Maintain mock-up during construction for workmanship comparison.

Delete one of the following two choices for final disposition of mock-up

#### Removal: Remove and legally dispose of mock-up when no longer required.

#### Incorporation: Mock-up may be incorporated into final construction upon Owner’s approval.

## Pre-Installation Meetings: Conduct with [Contractor, Architect, Fabricator, Installer and any other subcontractors] whose work involves cable railing system to verify project requirements, framing and support conditions, mounting surfaces, manufacturer's installation instructions, and warranty requirements.  Comply with Division 1 requirements.

# DELIVERY, STORAGE, AND HANDLING

Specifier Note: This Section should include special and unique product requirements. Coordinate article below with Division 1 Product Requirements Section.

## General: Comply with Division 1 Product Requirements Sections Ordering: Comply with manufacturer’s ordering instructions and lead time requirements to avoid construction delays.

## Delivery: Deliver in manufacturer's original, unopened, undamaged containers, identification labels intact.

## Storage and Protection: Store materials protected from exposure to harmful weather conditions and at temperature and humidity conditions recommended by manufacturer. Store cartons and panels in a secure location in a dry place at the project site.

# WARRANTY

Specifier Note: Coordinate article below with Conditions of the Contract and with Division 1 Closeout Submittals (Warranty) Section.

## Manufacturer’s Warranty: Submit, for Owner’s acceptance, manufacturer’s standard warranty document executed by authorized company official.

PART 2 PRODUCTS

Specifier Note: Retain article below for proprietary method specification. Add product attributes, performance characteristics, material standards and descriptions as applicable. Use of such phrases as “or equal” or “or approved equal” or similar phrases may cause ambiguity in specifications. Such phrases require verification (procedural, legal and regulatory) and assignment of responsibility for determining “or equal” products.

# I-SYS® STAINLESS STEEL CABLE PLANT SUPPORT SYSTEM

## Manufactured and sold by: Carl Stahl DécorCable Innovations, Inc., 2401 International Pkwy., Ste. B, Woodridge, IL USA 60517. Tel: 312-474-1100, Fax: 312-474-1789, E: sales@decorcable.com, Web: www.decorcable.com.

## Proprietary Products/Systems: I-SYS® Brand Stainless Steel Cable Plant Support System.

### Material:

#### Cable: Type 316 4mm Ø 4mm stainless steel 7x7 wire rope.

#### Fittings, Anchors, Hardware, and Accessories: AISI 304, 316 or 316L stainless steel.

Specifier Note: Determine and specify how your rope will be constructed by choosing fittings in Section 2 below, then add anchors, clamps, hardware, and accessories in Sections 3, 4, and 5 to specify your complete plant support system. Follow assembly length guidance in Section 6. Delete paragraphs not required. Contact Carl Stahl-DecorCable for assistance in determining the correct cable and end fittings for your application.

Swaged ends provide ultimate holding strength and smallest fitting size for all rope diameters. Field installed fittings allow for in-field design flexibility and are normally slightly larger in diameter with holding strength approaching swaged fittings. See our catalog for technical details.

### Rope End Fittings, Terminals, and Tensioners:

#### External Thread-Swaged RH Stock #850, LH Stock #855.

#### External Thread F30 Hammer Swaged-RH Stock #950, LH Stock#951

#### External Thread F50 Hammer Swaged-RH Stock #948, LH Stock#949

#### External Thread-Field Installed RH Stock #850, LH Stock #850.

#### Internal Thread-Swaged RH Stock #860, LH Stock #861.

#### Internal Thread-Field Installed RH Stock #860, LH Stock #860.

#### Swaged Fork (Clevis) -Stock #881

#### Fork with Internal Thread-Swaged RH Stock #812, LH Stock #811.

#### Fork and Swage w/Turnbuckle -Stock #870

#### Swaged Eye-Stock #880

#### Eye with Internal Thread-Swaged RH Stock #814, LH Stock #813.

#### Eye and Swage w/Turnbuckle -Stock #889

#### Compressed Loop w/o Thimble-Stock #801/803

#### Compressed Loop w/ Thimble-Stock #802/804

#### Loop Clamp w/ Thimble-Stock #874

#### Turnbuckle with Swaged External Thread ends Stock #829

#### Turnbuckle with F30 Hammer Swaged External Thread ends Stock #829

Specifier Note: Specify components for anchoring and controlling plant support system. See our catalog or contact Carl Stahl-DecorCable for more details concerning plant and weather loads, recommended anchoring systems.

### Support Components:

#### Spacer Bar w/M8 Internal Thread-Specify Length-Stock #919.

#### Cross Clamp-Specify Length-Stock #919.

#### Spacer Bar-Unthreaded 8mm Internal Bore-Specify Length-Stock #919.

#### Spacer Bar Support Link-Stock #834

#### Clamp Screw for M8 Spacer Bars-Specify Size-Stock #923

#### Ground Plate- Unthreaded-Stock #836

#### Cover Disk with Internal M8 Threads -Stock #836

#### Eye Bolt-Stock #837

#### Eye Nut-Stock #838

#### Fork Bracket-Stock #834

#### SS Adjustable Support to for EIFS facades-Stock #897

#### Plastic Pipe Support for EIFS facades-Stock #897-0690

#### Sealing Disk for Pipe Support-Stock #897-9

#### Sealing Ring for Pipe Support-Stock #897-8

Specifier Note: Choose and Specify to add strength and rigidity, aid rapid plant coverage, and increase aesthetics. For anchor systems, consult structural engineer and local building codes for appropriate anchor method. See our catalog or contact Carl Stahl-DecorCable for more details.

### Clamps and Plant Supports:

#### 90° Cross Clamp-Stainless Steel-Stock #858

#### Adjustable Cross Clamp-Stainless Steel-Stock #858

#### Adjustable Cross Clamp w/Internal Threads-Stainless Steel-Stock #858

#### Cross Clamp-UV Resistant Plastic-Stock #920

#### CS Cross Clamp for Large Ropes-Stock #858

#### Radial Disk with M6 Internal Threads-Stock #897

#### Climber Stud-UV Resistant Plastic-Stock #924

#### Rod/Rope Interface with M6 Internal Thread for 8mm Rod-Stock #921-0600-12

#### Stainless Steel Rod-Ø 4mm-Stock #922-0400

#### Stainless Steel Rod-Ø 8mm-Stock #922-0800

### Anchors and Hardware:

#### Washer-Specify Type-Stock #896

#### Hex Nut-Specify Type-RH Stock #892, LH Stock #893

#### Dome Nut-RH -Stock #894

#### Hex Head Bolt-Stock #843

#### Socket Head Bolt-Stock #844

#### Pan Head Screw-Stock #890

#### Dual Thread Screw-RH Stock #878, LH Stock #877

#### Rampa Nut for Wood, Stock #803

#### Threaded Rod (Headless Screw)-RH Stock #882, LH Stock #883

#### Wall Anchor for Masonry with Internal Thread RH Stock #803

#### Wall Anchor for Masonry with External Thread RH Stock #803

Specifier Note: Contact Carl Stahl-DécorCable salesperson or website for measurement templates and guidelines at 312-474-1100 or go to www.decorcable.com.

### Length:

#### Provide optimum adjustment in both directions by calculating final tendon lengths with allowance for tensioning fittings with 2/3 open and with 1/3 of thread length engaged.

#### Measure tendon length from center of pin to center of pin, or center of eye to center of eye.

# PRODUCT SUBSTITUTIONS

## Substitutions: No substitutions permitted.

# FITTINGS AND ACCESSORIES

## Accessories: Provide grommet, bushings, nuts, washers, turnbuckles, fittings and other components as required for system installation

# FABRICATION

## Stainless Steel Cables and Fittings shall be dimensioned and fabricated to specified size and labeled according to shop drawings and installer’s specifications.

## Preassemble items in shop to greatest extent practicable to minimize assembly at project site. Disassemble units only to extent necessary for shipping and handling limitations. Mark units for reassembly.

PART 3 EXECUTION

Specifier Note: Article below is an addition to the CSI SectionFormat. Revise article below to suit project requirements and specifier’s practice.

## MANUFACTURER’S INSTRUCTIONS

## Compliance: Comply with manufacturer’s product data, including product technical bulletins, product catalog installation instructions and product carton instructions for installation.

Specifier Note: Specify actions required to physically determine that conditions are acceptable to receive primary products of the section.

## EXAMINATION

## Site Verification of Conditions: Verify mounting condition of previously installed surfaces to ensure it is acceptable for product installation in accordance with manufacturer’s instructions. Do not begin installation until backup surfaces are in satisfactory condition.

## PREPARATION

## Supply items required to be cast into concrete or embedded in masonry with setting templates, to appropriate sections.

## Take field measurements after permanent end terminations are in place and prior to preparation of shop drawings and fabrication, to ensure fitting of work.

## INSTALLATION

## Install cable plant support system in accordance with manufacturer's instructions and the approved shop drawings.

## Provide anchorage devices and fittings to secure to in-place construction; including threaded fittings for concrete inserts, toggle bolts and through-bolts. Install all rope assemblies plumb, level, square, and taut.

## Anchor system to mounting surfaces as indicated on the drawings.

## Separate dissimilar materials with bushings, grommets or washers to prevent electrolytic corrosion.

## Use manufacturer’s supplied mounting hardware.

## Terminate and tension cable system in accordance with manufacturer’s instructions.

## Ensure ropes are clean, and without kinks or sags.

## After final adjustment provide tamper resistant locktight materials on all fittings.

## CLEANING

## Remove temporary coverings and protection of adjacent work areas.

## Clean installed products in accordance with manufacturer's instructions before owner's acceptance. Do not use chlorine-based or abrasive cleaners.

## Remove from project site and legally dispose of construction debris associated with this work.

## PROTECTION

## Protection: Protect installed product from damage during subsequent construction activities.

END OF SECTION