SECTION 05 73 00

ORNAMENTAL HANDRAILS AND RAILINGS

Show hidden Specifier Notes for best results

I-SYS® INOX Brand “IK-Pre Assembled” stainless steel railing cable system by Carl Stahl-DécorCable Innovations.

:

Carl Stahl-DecorCable Innovations LLC;

660 W. Randolph St.

Chicago, IL USA 60661

Phone:  800-444-6271

Fax: 312-474-1789

E-mail: sales@decorcable.com

Web: www.decorcable.com

This Product Specification is written in accordance with the Construction Specifications Institute (CSI) Format , including MasterFormat, SectionFormat and PageFormat. Optional text is indicated by brackets [ ]; delete optional text in final copy of specification. Specifier Notes are shown in red typically precede specification text; delete Specifier Notes in final copy of specification.

This Section specifies stainless steel railing infill cable system marketed under the I-SYS® tradename. Revise section number and title below to suit project requirements, local building codes, specification practices and section content. Refer to CSI MasterFormat for other section numbers and titles.

© 2006 Carl Stahl-DécorCable Innovations LLC

PART 1 GENERAL

# SUMMARY

## Section Includes:

### I-SYS IK Preassembled Stainless Steel Cable Railing System

## Related Sections:

Specifier Note: Edit following list according to project requirements.

### Section 4 - Masonry Anchoring and Reinforcing

### Section 5 - Metal Stairs

### Section 5 - Metal Railings

### Section 5 – Stainless Steel Wire Rope Assemblies

### Section 5 – Decorative Metal Railings

### Section 5 – Rooftop Fall Protection

# SYSTEM DESCRIPTION

## Performance Requirements: Provide I-SYS Stainless Steel Cable Railing System and mounting hardware which have been manufactured and installed to meet or exceed manufacturer’s and project performance criteria.

# SUBMITTALS

Specifier Note: This Section includes submittal of relevant data to be furnished by Contractor before, during or after construction. Coordinate this article with Architect’s and Contractor’s duties and responsibilities in Conditions of the Contract and Division 1 Submittal Procedures Section.

## Submit listed submittals in accordance with Conditions of the Contract and Division 1 Submittal Procedures Section.

## Product Data: Submit Manufacturer’s product data sheet for specified products.

## Shop Drawings: Show layout, sizes, dimensions, details, and installation of railing frame components. Include Details of rope attachment, tensioning methods, hardware, and tensioning and mounting methodology.

## Samples: Submit samples of rope and/or hardware, as required by specifier.

## Quality Assurance/Control Submittals:

### Test reports: Submit any test report demonstrating compliance with intended use and code requirements.

### Certificates: Submit manufacturer’s certificate that product meets or exceeds specified requirements

## Closeout Submittals: Submit the Following:

### Warranty: Submit manufacturer’s standard warranty documents

### Maintenance Data: Include manufacturer’s standard cleaning and maintenance instructions to avoid detrimental actions to finishes and performance.

# QUALITY ASSURANCE

Specifier Note: This Section should include prerequisites, standards, limitations and criteria that establish an overall level of quality for products and workmanship for this section. Coordinate with Division 1 Quality Assurance Section.

## Qualifications:

### Installer Qualifications: Installer should be experienced in performing work of this section and should have specialized in installation of work similar to that required for this project.

## Regulatory Requirements and Approvals:

### [Code Agency Name]

#### [Report or Approval Description]

## Mock-Ups: Install at project site or appropriate location a job mock-up using acceptable products and manufacturer approved installation methods. Obtain Owner’s and Architect’s approval of product, application, and workmanship standards. Comply with Division 1 Quality Control (Mock-Up Requirements) Section.

Specifier Note: Edit paragraph below when specifying mock-up requirements.

### Mock-Up Size: [Specify mock-up size and fixation requirements].

### Maintenance and Disposal: Maintain mock-up during construction for workmanship comparison.

Delete one of the following two choices for final disposition of mock-up

#### Removal: Remove and legally dispose of mock-up when no longer required.

#### Incorporation: Mock-up may be incorporated into final construction upon Owner’s approval.

## Pre-Installation Meetings: Conduct with [Contractor, Architect, Fabricator, Installer and any other subcontractors] whose work involves cable railing system to verify project requirements, framing and support conditions, mounting surfaces, manufacturer's installation instructions, and warranty requirements.  Comply with Division 1 requirements.

# DELIVERY, STORAGE, AND HANDLING

Specifier Note: This Section should include special and unique product requirements. Coordinate article below with Division 1 Product Requirements Section.

## General: Comply with Division 1 Product Requirements Sections Ordering: Comply with manufacturer’s ordering instructions and lead time requirements to avoid construction delays.

## Delivery: Deliver in manufacturer's original, unopened, undamaged containers, identification labels intact.

## Storage and Protection: Store materials protected from exposure to harmful weather conditions and at temperature and humidity conditions recommended by manufacturer. Store cartons and panels in a secure location in a dry place at the project site.

# WARRANTY

Specifier Note: Coordinate article below with Conditions of the Contract and with Division 1 Closeout Submittals (Warranty) Section.

## Manufacturer’s Warranty: Submit, for Owner’s acceptance, manufacturer’s standard warranty document executed by authorized company official.

PART 2 PRODUCTS

Specifier Note: Retain article below for proprietary method specification. Add product attributes, performance characteristics, material standards and descriptions as applicable. Use of such phrases as “or equal” or “or approved equal” or similar phrases may cause ambiguity in specifications. Such phrases require verification (procedural, legal and regulatory) and assignment of responsibility for determining “or equal” products.

# I-SYS® INOX STAINLESS STEEL CABLE HANDRAIL SYSTEM

## Manufactured and sold by: Carl Stahl DécorCable Innovations, Inc., 2401 International Pkwy., Ste. B, Woodridge, IL USA 60517. Tel: 312-474-1100, Fax: 312-474-1789, E: sales@decorcable.com, Web: www.decorcable.com.

## Proprietary Products/Systems: I-SYS® INOX “IK Preassembled” Stainless Steel Cable Handrail System.

### Material:

#### Cables: Type 316 stainless steel 7x7.

Specifier Note: 7x7 wire rope is used for most railing applications due to ease of use and flexibility to accommodate stairs and curves. Typically 3mm (1/8 inch) to 8mm (5/16 inch) is used for cable infill. Preassembled systems are easy to specify and are general less expensive. They include rope, end fittings and hardware. Select Assembly number from the following examples. Field Installed fittings increase specification flexibility where final field measurements will not be possible before installation. Field Installed fittings meet or exceed 90% of the ropes Maximum Breaking Load and can be used on SS Wire Rope, only. Not permissible for Stranded Wire. Specify IK assembly and rope diameter and delete choices not required. Consult Carl Stahl-DécorCable for additional information. For technical details and photos, go to www.decorcable.com.

### IK Rope Assemblies with Swaged or Field Installed End Fittings:.

#### Stock #IK-100-Swaged RH/RH External Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: Use for simple bolt through installations.

#### Stock #IK-101-Swaged RH/LH External Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: RH/LH external thread combination speeds tensioning.

#### Stock #IK-110-Swaged External Threads and Turnbuckles both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 barrel turnbuckles, nuts.

#### Notes: Standard two-turnbuckle setup for long cable runs for extra tensioning.

#### Stock #IK-120-Hammer Swaged F30 RH/RH Low Profile External Thread

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: External thread fitting is only 1-2mm greater in diameter for tight hole dimensions.

#### Stock #IK-121-Hammer Swaged F30 RH/LH Low Profile External Thread

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: External thread fitting is only 1-2mm greater in diameter for tight hole dimensions.

#### Stock #IK-125-Hammer Swaged F50 RH/RH Super Low Profile External Thread

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: External thread fitting is same ø as rope for tight hole dimensions.

#### Stock #IK-126-Hammer Swaged F50 RH/LH Super Low Profile External Thread

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: External thread fitting is same ø as rope for tight hole dimensions

#### Stock #IK-130-Hammer Swaged F30 External Threads and Turnbuckles both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 4mm, 5mm, 6mm.

#### Fittings and Hardware: Includes AISI 316 cylinder turnbuckles, nuts.

#### Notes: Low Profile two-turnbuckle setup for long cable runs through tight hole dimensions.

#### Stock #IK-140-Field Installed RH/RH External Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: Field installed ends warranted to 90% of rope MBL.

#### Stock #IK-141-Field Installed RH/LH External Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: Field installed ends warranted to 90% of rope MBL

#### Stock #IK-150-Swaged RH External Thread w/swaged radius head end stop

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: Radius end is nice finish detail on flat posts.

#### Stock #IK-160-Swaged RH External Thread w/swaged countersunk head end stop

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 hex nuts.

#### Notes: CS end stop provides flat finish detail on flat/square posts.

#### Stock #IK-170-Hammer Swaged F30 RH w/ Internal Radius End Stops both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 4mm, 5mm, 6mm.

#### Fittings and Hardware: Includes AISI 316 end stops and nuts.

#### Notes: All Internal Thread End Stops are RH only. Tightened with hex key.

#### Stock #IK-180-Hammer Swaged F30 RH w/ Internal Countersunk End Stops both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 4mm, 5mm, 6mm.

#### Fittings and Hardware: Includes AISI 316 end stops and nuts.

#### Notes: ALL Internal Thread End Stops are RH only. Tightened with hex key.

#### Stock #IK-190-Hammer Swaged F30 RH w/ Internal Ball Head End Stops both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm.

#### Fittings and Hardware: Includes AISI 316 end stops and nuts.

#### Notes: ALL Internal Thread End Stops are RH only. Tightened with hex key.

#### Stock #IK-200-Swaged RH/RH Internal Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: None included.

#### Notes: RH Internal threads are easy to install and accommodate many end conditions.

#### Stock #IK-201-Swaged RH/LH Internal Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: None included.

#### Notes: RH/LH Internal threads for quick tensioning.

#### Stock #IK-210- Field Installed RH/LH Internal Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: None included.

#### Notes: Field installed ends warranted to 90% of rope MBL

#### Stock #IK-211- Field Installed RH/LH Internal Thread both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: None included.

#### Notes: Field installed ends warranted to 90% of rope MBL

#### .

#### Stock #IK-300-Swaged RH/LH Internal Thread with Forks both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #871/872 forks, nuts.

#### Notes: Use Forks for mounting to flange type posts and for inclined stair applications

#### Stock #IK-305-Swaged RH/LH Internal Thread with CS Forks both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #945/946 CS forks, nuts.

#### Notes: Use Forks for mounting to flange type posts and for inclined stair applications

#### Stock #IK-310-Swaged Fork and Swaged Turnbuckles with Fork

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes barrel turnbuckle, #871/872 forks, nuts.

#### Notes: Ideal for Trellis and vertical suspension applications

#### Stock #IK-320-Swaged External RH/LH Thread with Turnbuckles with Fork both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes barrel turnbuckles, #871/872 forks, and nuts.

#### Notes: Use Forks for mounting to flange type posts and for inclined stair applications.

#### Stock #IK-340-Hammer Swaged F30 RH/LH with Internal Thread Fork both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #817/818 forks, and nuts.

#### Notes: Use Forks for mounting to flange type posts and for inclined stair applications.

#### Stock #IK-345-Hammer Swaged F30 RH/LH with Internal Thread CS Forks both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #917/918 CS forks, and nuts.

#### Notes: Use Forks for mounting to flange type posts and for inclined stair applications.

#### Stock #IK-400-Swaged RH/LH Internal Thread with Eyes both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #885/886 eyes, nuts.

#### Notes: Use Eyes in tandem with forks for free-articulation in inclined stair applications.

#### Stock #IK-405-Swaged RH/LH Internal Thread with CS Eyes both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #985/986 CS eyes, nuts.

#### Notes: Use Eyes in tandem with forks for free-articulation in inclined stair applications.

#### Stock #IK-410-Swaged Eye and Swaged Turnbuckles with Eye

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes barrel turnbuckle #885/886 eye, nuts.

#### Notes: Ideal for Trellis and vertical suspension applications

#### Stock #IK-420-Swaged External RH/LH Thread with Eyes and Turnbuckles both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes barrel turnbuckles, #885/886 eyes, and nuts.

#### Notes: Use Eyes in tandem with forks for free-articulation in inclined stair applications.

#### Stock #IK-430-Field Installed RH/LH Internal Thread with Eyes both ends

#### Rope Construction: AISI 316 stainless steel 7x7 wire rope.

#### Choose Rope Diameter: 3mm, 4mm, 5mm, 6mm, 8mm.

#### Fittings and Hardware: Includes AISI 316 #885/886 eyes, nuts.

#### Notes: Use Eyes in tandem with forks for free-articulation in inclined stair applications. Field installed ends warranted to 90% of rope MBL.

#### Stock #IKZ600 Both Sides External Thread Rolled

#### Rope Construction: AISI 316 stainless steel 1x19, 1x37 or 1x61 strand.

#### Choose Rope Diameter: 6mm, 8mm, 10mm, 12mm, 14mm, 16mm, 18mm, 22mm or 26mm.

#### Fittings and Hardware: Includes ?.

#### Notes:

#### Stock #IKZ604 Both Sides Turnbuckle With Fork Fitting

#### Rope Construction: AISI 316 stainless steel 1x19, 1x37 or 1x61 strand.

#### Choose Rope Diameter: 6mm, 8mm, 10mm, 12mm, 14mm, 16mm, 18mm, 22mm or 26mm.

#### Fittings and Hardware: Includes AISI 316 stainless steel turnbuckles with fork fittings.

#### Notes:

#### Stock #IKZ605 One Side Turnbuckle With Fork, Other Side Fork Swaged

#### Rope Construction: AISI 316 stainless steel 1x19, 1x37 or 1x61 strand.

#### Choose Rope Diameter: 6mm, 8mm, 10mm, 12mm, 14mm, 16mm, 18mm,   22mm or 26mm.

#### Fittings and Hardware: Includes AISI 316 stainless steel turnbuckle with forks.

#### Notes:

#### Stock #IKZ607 Both Sides With Fork Fitting Rolled

#### Rope Construction: AISI 316 stainless steel 1x19, 1x37 or 1x61 strand.

#### Choose Rope Diameter: 6mm, 8mm, 10mm, 12mm, 14mm, 16mm, 18mm, 22mm or 26mm.

#### Fittings and Hardware: Includes AISI 316 rolled fork fittings.

#### Notes:

Specifier Note: Contact Carl Stahl-DécorCable salesperson or website for measurement templates and guidelines at 312-474-1100 or go to www.decorcable.com.

### Length

#### Provide optimum adjustment in both directions by calculating final tendon lengths with allowance for tensioning fittings with 2/3 open and with 1/3 of thread length engaged.

#### Measure tendon length from center of pin to center of pin, or center of eye to center of eye.

# PRODUCT SUBSTITUTIONS

## Substitutions: No substitutions permitted.

# FITTINGS AND ACCESSORIES

## Accessories: Provide grommet, bushings, nuts, washers, turnbuckles, fittings and other components as required for system installation

# FABRICATION

## Stainless Steel Cables and Fittings shall be dimensioned and fabricated to specified size and labeled according to shop drawings and installer’s specifications.

## Preassemble items in shop to greatest extent practicable to minimize assembly at project site. Disassemble units only to extent necessary for shipping and handling limitations. Mark units for reassembly.

PART 3 EXECUTION

Specifier Note: Article below is an addition to the CSI SectionFormat. Revise article below to suit project requirements and specifier’s practice.

## MANUFACTURER’S INSTRUCTIONS

## Compliance: Comply with manufacturer’s product data, including product technical bulletins, product catalog installation instructions and product carton instructions for installation.

Specifier Note: Specify actions required to physically determine that conditions are acceptable to receive primary products of the section.

## EXAMINATION

## Site Verification of Conditions: Verify condition of previously installed support members to ensure they are acceptable for product installation in accordance with manufacturer’s instructions. Do not begin installation until backup surfaces are in satisfactory condition.

## PREPARATION

## Supply items required to be cast into concrete or embedded in masonry with setting templates, to appropriate sections.

## Take field measurements after permanent end terminations are in place and prior to preparation of shop drawings and fabrication, to ensure fitting of work.

## INSTALLATION

## Install rope assemblies in accordance with manufacturer's instructions and the approved shop drawings.

## Provide anchorage devices and fittings to secure to in-place construction; including threaded fittings for concrete inserts, toggle bolts and through-bolts. Install system plumb, level, square, and taut.

## Anchor system to mounting surfaces as indicated on the drawings.

## Separate dissimilar materials with bushings, grommets or washers to prevent electrolytic corrosion.

## Use manufacturer’s supplied mounting hardware.

## Terminate and tension cable system in accordance with manufacturer’s instructions.

## Ensure ropes are clean, and without kinks or sags.

## After final adjustment provide tamper resistant thread-locker on all threaded fittings.

## CLEANING

## Remove temporary coverings and protection of adjacent work areas.

## Clean installed products in accordance with manufacturer's instructions before owner's acceptance. Do not use chlorine-based or abrasive cleaners.

## Remove from project site and legally dispose of construction debris associated with this work.

## PROTECTION

## Protection: Protect installed product from damage during subsequent construction activities.

END OF SECTION