SECTION 05700

STAINLESS STEEL FLEXIBLE CABLE MESH

Show hidden Specifier Notes for best results

X-TEND® NEO Brand Stainless Steel Flexible Cable Mesh:

Carl Stahl-DecorCable Innovations LLC;

660 W. Randolph St.

Chicago, IL USA 60661

Phone:  800-444-6271

Fax: 312-474-1789

E-mail: sales@decorcable.com

Web: www.decorcable.com

This Product Specification is written in accordance with the Construction Specifications Institute (CSI) Format , including MasterFormat, SectionFormat and PageFormat. Optional text is indicated by brackets [ ]; delete optional text in final copy of specification. Specifier Notes are shown in red typically precede specification text; delete Specifier Notes in final copy of specification.

This Section specifies stainless steel flexible cable mesh marketed under the X-TEND® NEO tradename. Revise section number and title below to suit project requirements, local building codes, specification practices and section content. Refer to CSI MasterFormat for other section numbers and titles.

© 2006 Carl Stahl-DécorCable Innovations LLC

PART 1 GENERAL

# SUMMARY

## Section Includes: Stainless Steel Flexible Cable Mesh

## Related Sections:

Specifier Note: Edit following list according to project requirements.

### Section 4 - Masonry Anchoring and Reinforcing

### Section 5 - Metal Stairs

### Section 5 - Metal Railings

### Section 5 – Wire Rope Assemblies

### Section 5 – Decorative Metal Railings

### Section 6 – Wood Stairs and Railings

### Section 13 – Athletic and Recreation Safety Netting

### Section 13 – Fabric Structures

### Section 32 – Exterior Fences and Gates

# REFERENCES

Specifier Note: Edit following list according to project requirements.

## General: Standards listed by reference, including revisions by issuing authority, form a part of this specification section to extent indicated. Standards listed are identified by issuing authority, authority abbreviation, designation number, title or other designation established by issuing authority. Standards subsequently referenced herein are referred to by issuing authority abbreviation and standard designation.

## American Society for Testing and Material (ASTM International)

### ASTM A380 - Practice for Cleaning and Descaling Stainless Steel Parts, Equipment and Systems.

### ASTM A492 - Specification for Stainless Steel Rope Wire.

### ASTM A554 – Welded Stainless Steel Mechanical Tubing.

### ASTM A554 – Specification for Welded Stainless Steel Mechanical Tubing

### ASTM A555 - Stainless Steel Wire.

### ASTM E985 – Standard Specification for Permanent Metal Railing Systems and Stairs for Buildings

### ASTM F1145  - Specification for Turnbuckles, Swaged, Welded, Forged.

## Military Specification (MIL)

### MIL-C5688 - Pre-Stretching and Proof-Testing of Wire Rope Assemblies.

### MIL-W-83420 - Wire Rope, Flexible for Aircraft Control.

# SYSTEM DESCRIPTION

## Performance Requirements: Provide Stainless Steel flexible Mesh Guardrail Infill and mounting hardware which have been manufactured and installed to meet or exceed manufacturer’s and project performance criteria.

# SUBMITTALS

Specifier Note: This Section includes submittal of relevant data to be furnished by Contractor before, during or after construction. Coordinate this article with Architect’s and Contractor’s duties and responsibilities in Conditions of the Contract and Division 1 Submittal Procedures Section.

## Submit listed submittals in accordance with Conditions of the Contract and Division 1 Submittal Procedures Section.

## Product Data: Submit Manufacturer’s product data sheet for specified products.

## Shop Drawings: Show layout, sizes, dimensions, details, and installation of railing frame components. Include mesh aperture and rope dimensions, cable and mesh attachment hardware, tensioning devices, mounting methodology.

## Samples: Submit samples of mesh and support hardware, as required.

## Quality Assurance/Control Submittals:

### Test reports: Submit any test report demonstrating compliance with intended use and code requirements.

### Certificates: Submit manufacturer’s certificate that product meets or exceeds specified requirements

## Closeout Submittals: Submit the Following:

### Warranty: Submit manufacturer’s standard warranty documents

### Maintenance Data: Include manufacturer’s standard cleaning and maintenance instructions to avoid detrimental actions to finishes and performance.

# QUALITY ASSURANCE

Specifier Note: This Section should include prerequisites, standards, limitations and criteria that establish an overall level of quality for products and workmanship for this section. Coordinate with Division 1 Quality Assurance Section.

## Qualifications:

### Installer Qualifications: Installer should be experienced in performing work of this section and should have specialized in installation of work similar to that required for this project.

### Specifier Note: Paragraph below should list obligations for compliance with specific code requirements particular to this section. General statements to comply with a particular code are typically addressed in Conditions of the Contract and Division 1 Regulatory Requirements Section. Repetitive statements should be avoided.

## Regulatory Requirements and Approvals:

### [Code Agency Name]

#### [Report or Approval Description]

## Mock-Ups: Install at project site or appropriate location a job mock-up using acceptable products and manufacturer approved installation methods. Obtain Owner’s and Architect’s approval of product, application, and workmanship standards. Comply with Division 1 Quality Control (Mock-Up Requirements) Section.

Specifier Note: Edit paragraph below when specifying mock-up requirements.

### Mock-Up Size: [Specify mock-up size and fixation requirements].

### Maintenance and Disposal: Maintain mock-up during construction for workmanship comparison.

Delete one of the following two choices for final disposition of mock-up

#### Removal: Remove and legally dispose of mock-up when no longer required.

#### Incorporation: Mock-up may be incorporated into final construction upon Owner’s approval.

## Pre-Installation Meetings: Conduct meetings with [Contractor, Architect, Fabricator, Installer and any other subcontractors] whose work involves railing system to verify project requirements, framing and support conditions, mounting surfaces, manufacturer's installation instructions, and warranty requirements.  Comply with Division 1 requirements.

# DELIVERY, STORAGE, AND HANDLING

Specifier Note: This Section should include special and unique product requirements. Coordinate article below with Division 1 Product Requirements Section.

## General: Comply with Division 1 Product Requirements Sections Ordering: Comply with manufacturer’s ordering instructions and lead time requirements to avoid construction delays.

## Delivery: Deliver in manufacturer's original, unopened, undamaged containers, identification labels intact.

## Storage and Protection: Store materials protected from exposure to harmful weather conditions and at temperature and humidity conditions recommended by manufacturer. Store cartons and panels in a secure location in a dry place at the project site.

# WARRANTY

Specifier Note: Coordinate article below with Conditions of the Contract and with Division 1 Closeout Submittals (Warranty) Section.

## Manufacturer’s Warranty: Submit, for Owner’s acceptance, manufacturer’s standard warranty document executed by authorized company official.

PART 2 PRODUCTS

Specifier Note: Retain article below for proprietary method specification. Add product attributes, performance characteristics, material standards and descriptions as applicable. Use of such phrases as “or equal” or “or approved equal” or similar phrases may cause ambiguity in specifications. Such phrases require verification (procedural, legal and regulatory) and assignment of responsibility for determining “or equal” products.

# X-TEND® CXS STAINLESS STEEL FLEXIBLE CABLE MESH

## Manufactured and sold by: Carl Stahl DécorCable Innovations, Inc., 2401 Internationale Pkwy., Ste. B, Woodridge, IL USA 60517. Tel: 312-474-1100, Fax: 312-474-1789, E: sales@decorcable.com, Web: www.decorcable.com.

## Proprietary Products/Systems: X-TEND® Stainless Steel Flexible Mesh Handrail Infill

### Material: Type 316 stainless steel 7x7 wire rope joined with AISI 316 stainless steel ferrules.

Specifier Note: Select and specify one or more products from each section listed below and delete items not required. Mesh aperture up to 80mm is BOCA and ADA code compliant. Use 1.0mm cable size for aviaries, interior fixtures, and light duty applications. Use 1.5mm cable size for residential and light commercial/retail use. Use 2mm or 3mm cable size for public areas, zoo enclosures, and security applications. Contact Carl Stahl-DécorCable to obtain additional information, as needed. Retain, edit, or delete text below per project requirements and specifier’s practice.

### Cable Diameter x Mesh Aperture Dimensions

#### 1.5mm x 35mm, Stock #CX015035-S

#### 1.5mm x 40mm, Stock #CX015040-S

#### 1.5mm x 50mm, Stock #CX015050-S

#### 1.5mm x 60mm, Stock #CX015060-S

#### 1.5mm x 70mm, Stock #CX015070-S

#### 1.5mm x 80mm, Stock #CX015080-S

#### 1.5mm x 100mm, Stock #CX015100-S

#### 1.5mm x 120mm, Stock #CX015120-S

#### 1.5mm x 140mm, Stock #CX015140-S

#### 1.5mm x 160mm, Stock #CX015160-S

#### 1.5mm x 180mm, Stock #CX015180-S

Specifier Note: Select required paragraph(s) and delete paragraph not required. For most handrail infill applications, a horizontal mesh construction is preferred for ease of installation. Use Diagonal Grain for Staircase applications. Contact Carl Stahl-DécorCable for assistance in determining what option is best for your application.

### Direction (Grain) of X-tend Mesh:

#### Horizontal Mesh Direction.

#### Vertical Mesh Direction.

** NOTE TO SPECIFIER **  Select required paragraph(s) and delete paragraph not required. For best results and peak performance, X-tend must be evenly tensioned on a support frame on all sides. Use a solid or flexible support frame of adequate strength to resist deflection. Contact Carl Stahl-DécorCable for assistance in determining what option is best for your application.

### Support Frame Style

#### Round or Square Tubular Edge Supports constructed of Wood, Aluminum, Mild, or Stainless Steel. Supports to be spaced no more than 5 feet apart, depending on composition and size of support tubing.

#### I-SYS INOX 7x7 (or 7x19) construction Stainless Steel Wire Rope. Supports to be spaced no more than 5 feet apart, depending on size and construction of support ropes.

#### Other-Specify

# PRODUCT SUBSTITUTIONS

## Substitutions: No substitutions permitted.

## FITTINGS AND ACCESSORIES

## General: Attachment Cable Material: Type 316 stainless steel 7x7 (or 7x19) wire rope.

## Accessories: Provide grommet, bushings, washers, swaging ferrules, studs, receivers, fittings and other components as required for system installation.

# FABRICATION

## Infill Construction: Infill panels shall be dimensioned and manufactured to specified size and labeled according to installer’s specifications.

PART 3 EXECUTION

Specifier Note: Article below is an addition to the CSI SectionFormat. Revise article below to suit project requirements and specifier’s practice.

## MANUFACTURER’S INSTRUCTIONS

## Compliance: Comply with manufacturer’s product data, including product technical bulletins, product catalog installation instructions and product carton instructions for installation.

Specifier Note: Specify actions required to physically determine that conditions are acceptable to receive primary products of the section.

## EXAMINATION

## Site Verification of Conditions: Verify condition of railing and post system which has been previously installed under other sections, to ensure it is acceptable for product installation in accordance with manufacturer’s instructions. Do not begin installation until backup surfaces are in satisfactory condition.

## PREPARATION

## Supply items required to be cast into concrete or embedded in masonry with setting templates, to appropriate Sections.

## Take field measurements after permanent end terminations are in place and prior to preparation of shop drawings and fabrication, to ensure fitting of work.

## INSTALLATION

## Install mesh infill system in accordance with manufacturer's instructions and the approved shop drawings.

## Provide anchorage devices and fittings to secure to in-place construction; including threaded fittings for concrete inserts, toggle bolts and through-bolts. Install mesh panels plumb, level, square, and taut.

## Anchor mesh system to mounting surfaces as indicated on the drawings.

## Separate dissimilar materials with bushings, grommets or washers to prevent electrolytic corrosion.

## Use manufacturer’s supplied mounting hardware.

## Terminate and tension mesh panels in accordance with manufacturer’s instructions.

## Ensure mesh is clean, and without waves, kinks, or sags.

## Adjust frame support cable tension and connecting hardware.

## CLEANING

## Remove temporary coverings and protection of adjacent work areas.

## Clean installed products in accordance with manufacturer's instructions before owner's acceptance. Do not use chlorine-based or abrasive cleaners.

## Remove from project site and legally dispose of construction debris associated with this work.

## PROTECTION

## Protection: Protect installed product from damage during subsequent construction activities.

END OF SECTION